## Slide 1
Boost converter | Open-loop test setup
PR3 experimental connection diagram • Direct pulse injection at VGD
Oscilloscope
Built-in signal generator + CH1
Generator OUT
Pulse; vary duty cycle
CH1 probe
Measure Vout
DC supply 2.5 V / 3.5 V
Boost power stage (DUT)
Simplified from the supplied Altium schematic
L1
D1
Vbat
5V output
Q1
R5
GND
VGD
Pulse
CH1 tip
Supply +
Common GND: supply −, generator return, CH1 ground, board GND
Figure. Experimental connections for the duty-cycle sweep; node labels Vbat, VGD and 5V match the Altium schematic.